…Titel
The Physics of the plasma sheath

---
The space is filled with space plasma.
The plasma interacts with an object made of conducting material (spacecraft) which is immersed in the plasma.
A boundary zone forms around the body.
This boundary zone is called plasma sheath.
Basics

---
2 or 3 different currents flow to the spacecraft, depending on the environment.
In a steady state condition the, sum of the currents must be zero.
Depending on the magnitude of the photo-electron current, the spacecraft can be charged positively or negatively.
Depending on the charging, there are two different forms of the sheath possible.
-
-
+
Ion current
Electron
current
Photoelectron
current
Basics

---
No illumination --> only thermal electron- and ion-current.
At comparable temperatures the mean speed of the electrons will be higher.
--> more electrons hit the surface in a given time interval.
--> the S/C will be charged negatively.
--> the negative charge of the S/C pushes away the mobile electrons and attracts the ions.
--> an electron depletion zone forms around the S/C
--> the sheath thickness and S/C potential will adjust such that the currents have the same magnitude
Negatively charged spacecraft

---
The number of photo-electrons exceeds the number of thermal electrons.
-->The body builds a positive charge such that the number of photoelectrons reaching the plasma is roughly equal to the number of thermal electrons impacting on the surface.
All other photo-electrons are unable to cross the potential difference and fall back to the surface.
These photoelectrons form an electron sheath.
They do not contribute to the photo-electron current.
Positively charged spacecraft

---
The currents can be estimated.
All thermal electrons reach the surface, while only photoelectrons with a certain minimum energy.
The photoelectrons are roughly Maxwell distributed.[Grard 1973]
iph ...current density at the surface.
Arel...relative illuminated area cross section.
The potential of the spacecraft can be deduced by equating thermal and photo-electron current.
The currents

---
The photo-electron density at the surface can be found by using .
Equilibrium: Produced electrons=impacting electrons (ignoring ions)
A possible way to estimate the sheath thickness.
The densities

---
The distribution of the photo-electron density.
The density of the thermal electrons can be derived as before.
The heavy ions are assumed not to be influenced by the potential gradient.
The densities

---
Boundary Conditions
1D flat surface approximation.
Substitution of the densities results in a Poisson equation.
The governing differential equation

---
Taylor expansion.
Assuming quasi-neutrality.
Only valid for small potential energies.
The solution is the sum of an exponential function and a constant.
Does not fulfill the boundary conditions.
One can define the shielding length.
The linearized equation

---
Spacecraft antennas are usually coupled to the surrounding space plasma.
The electromagnetic coupling can be modeled by a system of a resistance and a capacitance.
In rarefied plasma the coupling can not take place without photoelectrons.
The sheath thickness must not be larger than the antennas.
[Bale et. al. 2007]
Spacecraft antennas

---
The expressions for the positively charged spacecraft.
εr is the relative impedance tensor which depends on the model used.
Changes continuously along the sheath.
As a first approximation the mean value could be used.
Positively charged spacecraft

---
STEREO operates in solar wind conditions at 1AU.
The photo-electron production rate is higher than the thermal electron impact rate. --> positive charge.
iph...10-4Am-2 [Fahrleson 1967]
Arel...0.5
l=6m
d=1in (0.0254m) on average
Mean energy of photo-electrons=1.5eV [Grard 1973]
Mean energy of thermal electrons=10eV
-->V=5.5V
ne=106m-3
-->nph(0)=2x108m-3
-->2.5% of the photo-electrons reach the plasma.
-->λsh =0.6m or 0.4m, depending on the method.
Application

---
Using the appropriate equations, one finds:
  - Rs=0.2MΩ
  - Cs=87pF
Via these parameters the sheath can be included into the numerical antenna calibration (wire-grid).
Computation of the impedances show that the inclusion of the sheath has an effect.
Application

---
Comparing the location of the second resonance of antenna Ez with measured data shows that the inclusion of the sheath capacitance has a corrective effect.
Further and more accurate data is needed to verify the model.
Application

---
The surface of a body immersed in space plasma interacts in a complicated way with the plasma.
The body is charged negatively or positively and a sheath is formed.
Models approximating the physics of the electron sheaths were derived and partly solved.
Representing the sheath by a combination of resistivity and capacitance, the coupling of the antenna to the space plasma can be incorporated into the numerical antenna calibration.
As an example, the STEREO/WAVES antennas were used.
The results are promising, but we have to validate the models used.
Many estimations have to be used in the models.
A uniform sheath around the spacecraft has been assumed.
The velocity of the spacecraft has been neglected.
Final Remarks

---
Thank You for Your attention !
The End