The STEREO/WAVES antenna calibration
On the calibration of spacecraft antennas
Comparison and discussion of different methods
       Oswald, T.H. (1), Rucker (1), W. Macher (1), A. Lecacheux (2), J.L. Bougeret (2), M.L. Kaiser (3), K. Goetz (4)
(1) IWF/OEAW thomas.oswald@oeaw.ac.at
(2) Observatoire de Paris-Meudon, France
(3) NASA/GSFC Greenbelt, MD, USA
(4) University of Minnesota, USA

---
The STEREO mission
Antennas on spacecraft
Two kinds of antenas:
  - For communication
  - For scientific experiments
Scientific antennas often used to receive natural radiation
Sometimes direction finding is performed

---
Why is antenna calibration necessary ?
Why is antenna calibration necessary ?
To perform “Direction Finding”(DF), antenna properties must be known to a high degree of accuracy
The receiving properties can be quantified by the effective length vector
The effective length vector represents the antenna as it behaves electrically
It is influenced by the geometry of the spacecraft
Depends, in general, upon frequency and direction of incidence and is a complex vector, but at low frequency it can be treated as a constant real vector
In this quasistatic range, DF is possible

---
Methods to determine the effective length vector
Methods to determine the effective length vector
Numerical electromagnetic code
Rheometry
The EMC chamber
In-flight Calibration

---
The numerical method 1
The spacecraft is modelled as a grid of wires
Then the currents along these wires are computed
On base of the current distribution, all other antenna properties (effective length vectors, impedances, power patterns) can be calculated

---
The numerical method
The numerical method 1

---
Computation of the current distribution
Computation of the current distribution 1
The equation governing the current distribution is the electric field integral equation (EFIE), or the reaction integral equation
Simplifications:
  - Thin currents along the center of the wires
  - No transverse currents

---
The numerical method 2
The spacecraft is modelled of patches
Then the surface currents on each patch are computed
On base of the current distribution, all other antenna properties (effective length vectors, impedances, power patterns) can be calculated

---
The numerical method 2

---
Computation of the current distribution 2
The equation governing the current distribution is the magnetic field integral equation (MFIE)
Disadvantage: Longer computing time
Advantage: Better results in the high frequency range

---
The Method of Moments
The Method of Moments
The Method of Moments (MoM) can be used to solve integral equations
A modified version of the antenna scatterers analysis program (ASAP) and CONCEPT II are used to calculate the currents
Only CONCEPT II can deal with patches

---
The Matlab toolbox
Further calculations
The effective length vectors, impedances and power patterns are calculated by Matlab routines created in the space research institute
Calculations were performed for open feeds and base capacitances of 90pF

---
Rheometry
A gold-plated model of the spacecraft is submerged into a water tank
A low-frequency electric field is applied
The response (induced voltage) of the antennas is measured as a function of spacecraft orientation
The effective length vectors and the antenna impedances can be computed from the data
Open feeds are intrinsically included in the method
Rheometry is only applicable for the quasi-static limit

---
Rheometry
Rheometry

---
Our model
Some models

---
The EMC chamber
In the EMC (electromagnetic cleanliness) chamber a scale model is illuminated by coherent electromagnetic radiation.
The respons of the antennas is measured.
Different frequencies can be dealt with.

---
The EMC chamber

---
Inflight calibration
A known radio source, natural or manmade, is used to calibrate the antennas after launch
The spacecraft should make an appropriate roll manoeuvre to measure the dependence of the respons as a function of orientation

---
Overview

---
The results
The results in case of the stereo spacecraft

---
The impedances: Spacecraft A
The impedances

---
Thank You for Your attention !