The STEREO/WAVES antenna calibration
The STEREO/WAVES antenna calibration
Final Results
       Oswald, T.H. (1), W. Macher (1), H.O. Rucker (1), and the SWAVES team
Space Research Institute Graz/Austrian Academy of Sciences thomas.oswald@oeaw.ac.at

---
The STEREO mission
Two spacecraft, one ahead and one behind earth,slowly drifting apart at a rate of 22 degrees by year
To extend our knowledge about the physics of the solar system
Research on space weather, CMEs and sun-earth-connection (SEC)
For the first time stereoscopic methods are used which include remote and in-situ measurements of the same events

---
The STEREO mission

---
SWAVES
Measures electric fields
Frequency quasi-static-16MHz+2 fixed frequencies at 30.025 and 32.025MHz
Measures electron density and temperature with quasi thermal noise analysis
3 orthogonal monopole-stacer-antennas, directed away from the sun, 6m length
“Direction Finding” (DF) mode provides all auto- and cross correlation parameters
2 spacecraft render it possible to pinpoint the source of the EM radiation via triangulation
The equipment on the 2 s/c will track those radio sources from less than 2 RS to 1AU and beyond

---
SWAVES antennas
The Goal: Correct data interpretation
Influence of the spacecraft body
Effective length vectors and impedance- or capacitance matrices
These quantities were determined and analyzed numerically and experimentally
[Speaker Notes: Due to the Due to the influence of the spacecraft body, the properties of the antennas are different than those of stand-alone monopoles which point in the same direction In particular the effective length vectors and impedance- or capacitance matrices are valuable parameters These quantities were determined and analyzed numerically and experimentally]

---
The STEREO mission
STATUS QUO
We finished the ASAP project for the determination of the reception properties of the WAVES antennas on-board the two STEREO spacecraft.
The numerical and experimental procedures are completed
The interpretation of the results and the publication is not yet complete
The capacitances have to be determined numerically

---
Methods to determine the effective length vector
Numerical electromagnetic code
Rheometry
The anechoic chamber
In-flight Calibration

---
The experimental method :
Rheometry
A gold-plated model of the spacecraft is submerged into a water tank
A low-frequency electric field is applied
The response (induced voltage) of the antennas is measured as a function of spacecraft orientation
The effective length vectors and the antenna impedances can be computed from the data
Rheometry is only applicable to the quasi-static limit

---
Rheometry
Rheometry

---
Rheometry

---
Our model
Our model

---
The coordinate system

---
The coordinate system

---
The coordinate system

---
Rheometry results

---
Rheometry results
open feeds
loaded feeds

---
The numerical method
The numerical method

---
The numerical method

---
The numerical method
The spacecraft is modeled as a grid of wires or patches
Then the currents along these wires/patches are computed
This calculation is done with ASAP (wires) and CONCEPT II (wires and patches)
On base of the current distribution, all other antenna properties (effective length vectors, impedances) can be calculated with MATLAB routines

---
Computation of the current distribution
Computation of the current
distribution
The equation governing the current distribution is the electric field integral equation (EFIE. CONCEPT), or the reaction integral equation (RIE, ASAP)
For patches, the magnetic field integral equation (MFIE, CONCEPT) is used
The antenna is excited at the feed
Due to reciprocity, the receiving antenna results in the same current distribution as the transmitting

---
Computation of the antenna
properties
Calculations were performed for open feeds and base capacitances of 90pF
A correction for the real antenna diameters has to be applied on the ASAP results. CONCEPT can deal with real antenna diameters.

---
Numerical Results:
The quasi-static limit (ASAP)

---
Numerical Results:
The quasi-static limit (CONCEPT)

---
Experimental Results

---
Numerical Results:
The quasi-static limit

---
Numerical Results:
The quasi-static limit

---
Numerical Results:
The quasi-static limit

---
Numerical Results:
The quasi-static limit

---
Numerical Results:
The quasi-static limit

---
Numerical Results:
The quasi-static limit

---
Numerical Results:
The Effect of changing the model 1

---
Numerical Results:
The Effect of changing the model 2

---
Variation due to the HGA orientation

---
Relative deviation of the perpendicular component of the effective length vector

---
Relative deviation of the perpendicular component of the effective length vector

---
Relative deviation of the perpendicular component of the effective length vector

---
Relative deviation of the perpendicular component of the effective length vector

---
Relative offset from the quasi-static case
average
maximum

---
The impedances: Spacecraft A
The self-impedances(open)

---
The self-impedances(loaded)

---
Relative Gain Patterns

---
The results
Summary
The following parameters have been determined and investigated:
Open port transfer matrices
Antenna capacitances
Transfer matrices of the loaded antennas
The change of the results due to variation of the spacecraft structure
The effect of the orientation of the HGA
An estimation of the upper frequency limit below which the quasi-static result can be used
A new technique of correcting for inexact modeling of the antenna radii.
An estimation of the surface impedance of the rheometry model
The reception patterns at the FFR frequencies
[Speaker Notes: Experimental method and 2 numerical methods merits: rheometry : more details numerical method: variation of model patches: longer computing time but higher accuracy]